## Slide 1: MCTE 3104 Mechatronics Interfacing Lab
Experiment no. 2: Interfacing Analog Signals and Servos with ATMEGA and Raspberry Pi

## Slide 2: Outline
Analog Signals
Servos
Serial UART communication

## Slide 5
ADC – Analog to Digital Converter
ADC is a very useful feature that converts an analog voltage on a pin to a digital number.
The Arduino Uno board has 6 analog input pin.
ADCs on the Arduino is a 10-bit resolution meaning it has the ability to detect (2^10) 1,024 discrete analog levels.
ADC with 8 steps resolution 2^3 = 8

## Slide 6
Reading Analog input
Simple Analog input read using Arduino Library
A0
5V

## Slide 7
SERVO
Working principle
There is a minimum pulse, a maximum pulse, and a repetition rate.
The servo motor expects to see a pulse every 20 milliseconds (ms) and the length of the pulse will determine how far the motor turns.
A 1.5ms pulse will make the motor turn to the 90° position.
Shorter than 1.5ms moves it in the counter clockwise direction toward the 0° position.
Any longer than 1.5ms will turn the servo in a clockwise direction toward the 180° position.
https://www.jameco.com/jameco/workshop/howitworks/how-servo-motors-work.html
More reading:

## Slide 8
Controlling servo using Arduino Library

## Slide 9
Serial communication on Atmega328x
UART (Universal Asynchronous Receiver Transmitter)
Full duplex asynchronous serial communication
• RX at pin0 on the Arduino
• TX at pin1 on the Arduino
Advantages
Simple and Bidirectional
Disadvantages
Supports only one to one communication only
Note: while Atmega328x has only one hardware UART feature, Arduino ‘SoftwareSerial’ allows you to enable ‘software’ UART communication on other pins as well.
Connection configuration

## Slide 10
Serial communication on Arduino
Run this code and open the serial monitor. Observe and explain what happened?
Connect 2 Arduinos as the following and run the code on both devices. Observe and explain what happened?
10
11
Arduino
10
11
Arduino

## Slide 11
Serial communication Python to Arduino

## Slide 12
Judging from the Raspberry Pi Pinout in the next slide, can you figure out if a Raspberry Pi can support UART communication?
ls /dev/tty*

## Slide 14
http://www.toptechboy.com/raspberry-pi/raspberry-pi-with-lesson-26-controlling-gpio-pins-in-python/
Picture taken from
To begin using the Raspberry Pi GPIO, we first need to know Raspi's GPIO numbering system. The two inner columns (labelled pin#) in the chart shows the ‘physical pin number’ where as the outer two columns (labelled GPIO#) of the chart shows you the ‘BCM number’ (Broadcom numbering scheme).

## Slide 15
Use the same Python code on the raspi to communicate with the Arduino.
Hint: you need to change the ‘COMx’ bit of the code to the one raspi establishes.
Use this command to list all COM port in raspi: ls /dev/tty*