## Slide 1: MCTE 3104 Mechatronics Interfacing Lab
WEEK 5: Serial USB – UART communication

## Slide 2: Outline
Serial Communication (USB <-> UART)
  PC <-> Arduino
  Raspi <-> Arduino
Serial Communication (Device UART <-> Device UART)
  Arduino <-> Arduino
Serial UART Arduino Software Serial Library
  Arduino <-> Bluetooth

## Slide 5
Typical device to PC interfacing
USB-UART
converter
TX
RX
GND
  When a device is connected a ‘COM’ port is established at the PC

## Slide 6
USB – UART Converter
ATMEGA16U2
CH340G
FTDI - FT232RL

## Slide 7
  You can access these established ‘COM’ port using free software such as TeraTerm, SSCOM32, etc..

## Slide 8
  Send command from PC to turn On and Off an LED attached to the Arduino
  Since the Arduino is programmed to listen to the UART port and turns on on-board LED on when it receives ‘1’ and turns off on-board LED when it receives ‘0’.
  You can send command ‘1’ or ‘0’ using free software such as SSCOM32 or write Python script to talk to the Arduino
  Task: Use Python script on Raspi to communicate with Arduino to turn On and Off on-board LED

## Slide 9
Typical device to Device (UART) – Device (UART) interfacing

## Slide 10
Simple device to Device (UART) – Device (UART) interfacing
Device #1
Device #2

## Slide 11
Simple device to Device (UART) – Device (UART) interfacing
Device #1
Device #2

## Slide 12
Arduino SoftwareSerial Library
  Since the Hardware UART chip is connected to 0 and 1 which also goes to the computer via USB connection often time we want to use this port for debugging purposes by displaying on the serial monitor.
  SoftwareSerial library allows user to enable any digitial i/o pin to allow serial communication.
  You can use this to allow UART communication to other devices
  Task: Try now communicating with softwareserial UART instead of hardware UART